## Slide 1: CG3207 Lab 4 OVERVIEW
Ian Isaiah Tan, Lynthia Chai, Monday Group 10
Demo on Hardware
If SW[0] = 0
Does not start
Else
// 16 DP instr (with pipeline + control hazard)
Start hardware showcase
Enhancement 1
Overview
Enhancement 2
Thank you!

## Slide 2: Pipeline with Hazard
Architecture
Enhancement 1
Overview
Enhancement 2
Thank you!
Fetch
Decode
Execute
Memory
Write
Notes: Single Cycle vs Pipeline:
  Single Cycle: all instr run in single cycle
  Pipeline: all instr run by pipeline in 5 stages
    Fetch, Decode, Execute, Memory, Writeback
  Rationale: Improve throughput after steady state  latency of each instr not reduced but increased
ALU: Recoded to accommodate 16 instructions

## Slide 3: Pipeline with Hazard
Hazard Unit
Enhancement 1
Overview
Enhancement 2
Thank you!
Stall: “freeze” data at particular stage  deassert write
  E.g. 1st instr is LDR, 2nd instr is ADD, and if 1st instr not ready, how to ADD?
  Rationale: if next instr needs data before it is ready, there will be trouble
Flush: clear pipeline register  basically flush values down toilet
  E.g. in case it branches, then we cannot use the current set of instr anymore, need to “reset”
  Rationale: in case it changes stage when we want to stall  u need to clean the room before the next person use it.
Data Forward: take result from earliest stage and forward to functional units
  E.g. M & W are both later pipeline stages  Choose M
  Rationale: better to take from “more present” & pass to where it is needed
  When: only if instruction in M or W write to register (E.g. B / STR does not write)
Notes: Single Cycle vs Pipeline:
  Single Cycle: all instr run in single cycle
  Pipeline: all instr run by pipeline in 5 stages
    Fetch, Decode, Execute, Memory, Writeback
  Rationale: Improve throughput after steady state  latency of each instr not reduced but increased
ALU: Recoded to accommodate 16 instructions
Stall vs Flush:
  Stall: “freeze” data at particular stage  deassert write
  Flush: clear pipeline register  basically flush values down toilet

## Slide 4: Pipeline with Hazard
ALU
Enhancement 1
Overview
Enhancement 2
Thank you!
Original: ALUControl = 2 bits as lesser instr to accomodate
Edited: ALUControl = 4 bits as 16 instr to accommodate
Flags: Updated as usual
Rationale: Must tell the ALU how to compute based on instr info
Notes: Single Cycle vs Pipeline:
  Single Cycle: all instr run in single cycle
  Pipeline: all instr run by pipeline in 5 stages
    Fetch, Decode, Execute, Memory, Writeback
  Rationale: Improve throughput after steady state  latency of each instr not reduced but increased
ALU: Recoded to accommodate 16 instructions

## Slide 5: Branch Prediction
Architecture
Enhancement 1
Overview
Enhancement 2
Thank you!
Check if mispredict or not

## Slide 6: Branch Prediction
Saturation Counters
Enhancement 1
Overview
Enhancement 2
Thank you!
Notes: A 2-bit scheme can give 90% accuracy since a prediction must be wrong twice before the prediction bit is changed

## Slide 7: Branch Prediction
General Simulation
Enhancement 1
Overview
Enhancement 2
Thank you!
BTA_Mispredicted = 1: predicted destination (aka BTA) is wrong
Branch_Mispredicted = 1: predicted branch is wrong
Note: Destination prediction is correct afterwards because BHT store truncated PC instr to check

## Slide 8: Branch Prediction
Zoomed Simulation
Enhancement 1
Overview
Enhancement 2
Thank you!
Iteration 1
Iteration 2

## Slide 9: Branch Prediction
Where does it branch to
Enhancement 1
Overview
Enhancement 2
Thank you!

## Slide 10: Branch Prediction
Where does it branch to
Enhancement 1
Overview
Enhancement 2
Thank you!
DOWHILE Branch First Encounter – BTA and Branch predicted wrongly [Information stored in BHT]
Iteration 1
Iteration 2
DOWHILE Branch Second Encounter –Branch predicted wrongly prediction bit changed
DOWHILE Branch Correct predictions – Wrong Twice Already!
Assumes DOWHILE Branch but does not Branch to DOWHILE
Branch to SELECTBRANCH – Wrong prediction [Information stored in BHT]
Branch to WHILE – Wrong prediction [Information stored in BHT]
Process repeats itself like the first two encounters of DOWHILE
Subsequently, BTA and B is stored, there are occasional Branch Mis-prediction but that is expected when we change loops – must be wrong twice to update prediction bit

## Slide 11: Thank you!
Enhancement 1
Overview
Enhancement 2
Thank you!